## Slide 1: TS1 Components Testing
Library development in Visual Components
25.10.24

## Slide 2: Overview
Library Development of TS1 Components
Testing
Release
Components Availability
All TS1 components are available for testing
10/2023
Evaluation of product information
Planning of development
Specifications of simulation components
TS1 Evo development
Verification testing
Current Stage
Creating demonstration models
Validation Testing
Evaluation of PRM
Documentation
Provide models to Visual components
(Unit test)
(Interface test)
V-Model Framework for System development

## Slide 3: V-model for Library development
Testing of TS1 Components
Requirement Analysis
System Design
Architecture Design
Component Design
Implementation
Unit Testing
Interface testing
System testing
Acceptance testing
Validation
Verification
The Verification & Validation (V-model) provides a formal framework for system development to ensure validity.

## Slide 4: General Testing Phases
Testing of TS1 Components
Alpha test : Done after implementation phase, to check if all parameters and limitations are correctly implemented and general functional testing of modelled components.
Beta test : Done after unit and interface testing, involves creation of basic models to check functionality of modelled components working together.
Release test : Validating modelled components by recreating a use case model with the new components.

## Slide 5: Testing Phases
Components Availability: Checking if all TS1 components are modelled as per MTPro.
Verification testing: Consists of Unit test (Parameter Validation & Geometric evaluation) and Interface test.
Creating demonstration models: Utilizing the modelled components to verify the functionality of the components by creating basic models.
Validation Testing: Testing the entire system by recreating use case model using the TS1 components for validation.
Evaluation of PRM: The developed library components are provided to product management for evaluation.
Testing of TS1 Components

## Slide 6: Phase 1 : Checking Component Availability for Testing
Component in MTPro
Modelled Component in VC
Conveyor Unit
Section (ST 1)
Drive (AS 1)
Return Unit (UM1)
Testing of TS1 Components

## Slide 7: Phase 1 : Checking Component Availability for Testing
Component in MTPro
Modelled Component in VC
Legset (SZ 1)
Legset (two tracks)
Legset (SZ 1/L)
Testing of TS1 Components

## Slide 8: Phase 1 : Checking Component Availability for Testing
Component in MTPro
Modelled Component in VC
Workpiece Pallet (WT 1/K)
Workpiece Pallet (WT 1/S)
Workpiece Pallet (WT 1/P)
Testing of TS1 Components

## Slide 9: Phase 1 : Checking Component Availability for Testing
Component in MTPro
Modelled Component in VC
Position Unit (PE 1)
Lift Position Unit (HP 1/P h=15)
Lift Position Unit (HP 1/P h=0…50)
Testing of TS1 Components

## Slide 10: Phase 1 : Checking Component Availability for Testing
Component in MTPro
Lift Transfer Unit (HQ 1/U)
Stop Gate (VE 1)
Stop Gate (VE 1/V)
Modelled Component in VC
Testing of TS1 Components

## Slide 11: Phase 1 : Checking Component Availability for Testing
Component in MTPro
Curve CU 1/90
Curve KU 1/90
Curve KU 1/90 (KE 1/O-90)
Modelled Component in VC
Testing of TS1 Components

## Slide 12: Phase 1 : Checking Component Availability for Testing
Component in MTPro
Curve KU 1/180
Curve KU 1/180
(KE 1/O-180)
Modelled Component in VC
Testing of TS1 Components

## Slide 13: Phase 1 : Checking Component Availability for Testing
Component in MTPro
Modelled Component in VC
BS 1
BS 1/M
BS 1/T
BS 1/S
Testing of TS1 Components

## Slide 14: Phase 2 : Verification Testing
Unit test (Parameter Validation & Geometric Evaluation):
Verifying if all the associated parameters/attributes are properly defined and are within the required constrained limits for any individual component.
The attributes along with their data types are listed for specific variant of the component as available in MTPro and Visual Components.
The component properties, data types, default values and their limitations are counter checked for variation against the properties given in MTPro.
Additionally, evaluation of geometric changes upon manipulation of these attributes are also checked for variation.
Testing of TS1 Components

## Slide 15: Phase 2 : Verification Testing
Unit test (Parameter Validation & Geometric Evaluation):
A comparison excel sheet for the data available in MTPro and Visual Components is prepared as shown below.
TS1_Library_Testing.xlsx
Testing of TS1 Components

## Slide 16: Phase 2 : Verification Testing
2. Interface test:
Interface testing focuses on whether individual components interact with other components as intended.
Individual components are connected to each other and tested to verify if its functioning with the expected behavior.
To check different functionalities of the component, a structured question-based approach can be used such that each question is associated with a test to verify this functionality.
Each component will have several functionality questions and tests to verify it. The results of which are noted down in TS1_Library_Interface, Functionality test.xlsx
Testing of TS1 Components

## Slide 17: Phase 3 : Creating basic demonstration models
Testing of TS1 Components